## Slide 1: DeepAuto: A Hierarchical Deep Learning Framework for Real Time Prediction in Cellular Networks Authors: Abhijeet Bhorkar, Ke Zhang, Jin Wang
October 3, 2019

## Slide 2: Mobility Network Automation
Real time KPIs,
Historical counters, network alarms
Mobile Network optimization and automation is essential to improve network performance, reduce OPEX and keep up with demand, delivery & service.
Predictions
Control actions
AI
ONAP, RIC

## Slide 3: RAN Automation use cases
Energy savings (sleeping cell)
Load balancing
Scheduler optimization
Adaptive stream saver
Traffic offload
Handover optimization
Energy savings (sleeping cell)
Scheduler optimization
Adaptive stream saver

## Slide 4: Goals
  Include impacts of network configuration changes and external influence
  Framework should be able to predict real time
Capture multi-scale temporal and spatial information
Predict KPIs for different history and horizon combinations
Design a scalable reusable accurate* prediction framework to predict RAN KPIs
More accurate estimate results in better adaptation decisions
Xuan Kelvin et al, “Can Accurate Predictions Improve Video Streaming in Cellular Network”

## Slide 5: DeepAuto: Architecture of Prediction System
Coarse, longer delay data is used for mid term (hour-week) prediction.
Finer, shorter delay data is used for short term (second-mins) prediction.
Short Term Predictor
(sec-hour)
Real-Time Collector
LTE/5G Cell
15-min PM Data Collector
Long Term Predictor
(hour-week)
Prediction
API Gateway
DeepAuto
Notes: CIM – Common Information Model

## Slide 6: DeepAuto: Reusable prediction engine using deep learning
The objective of reusable prediction engine is to provide short-term (seconds to few mins) and long-term (hours, days, weeks) forecasts of various cell level and UE level KPIs.
The problem can be framed as time-series prediction and in general using Nonlinear Autoregressive with exogenous inputs (NARX) framework.
Past values of same series
Current and past values of exogeneous series
We have designed Long Short-Term Memory (LSTM) based framework for the prediction tasks.
LSTM frameworks have shown benefits over statistical frameworks such as Autoregressive integrated moving average (ARIMA) at the cost of increased complexity [1].
Traditional machine learning models such as random forest models cannot capture long term dependencies.
Proposed LSTM based architecture for reusable analytics
[1] LSTM network: a deep learning approach for short-term traffic forecast

## Slide 7: Evaluation of DeepAuto
We illustrate our work using most important cell level KPIs including cell load prediction and radio channel quality prediction.
  Key applications such as adaptive scheduler selection and cell load balancing will be enabled using cell load and channel quality KPI prediction
Cell load prediction: The objective is to predict average Cell PRB utilization in the next 1 min, 15 min and 1 hour for each cell.
Radio channel quality prediction : The objective is to predict RSRQ distribution in the next 5 mins for each cell.

## Slide 8: Cell Load Prediction (1)
cell_name | timestamp | cell_prb_util_percent_dl | active_ue_dl | cell_bitrate_kbps_dl | ENODEB | EARFCN_DL | DL_CH_BANDWIDTH | MAX_TX_POWER | LATITUDE | LONGITUDE | ALTITUDE | MARKET_CLUSTER | MARKET | SW_VERSION
CAL00013_2A_1 | 5/22/2018 0:00 | 53.13 | 1.49 | 5438 | CAL00013 | 2200 | 10000 | 490 | 32.7306694 | -117.1596778 | 84.2 | SAN DIEGO/LAS VEGAS | SAN DIEGO | CXP102051_27_R21F24
CAL00013_2A_1 | 5/22/2018 0:01 | 46.96 | 1.25 | 1153 | CAL00013 | 2200 | 10000 | 490 | 32.7306694 | -117.1596778 | 84.2 | SAN DIEGO/LAS VEGAS | SAN DIEGO | CXP102051_27_R21F24
CAL00013_2A_1 | 5/22/2018 0:02 | 52.45 | 1.57 | 2900 | CAL00013 | 2200 | 10000 | 490 | 32.7306694 | -117.1596778 | 84.2 | SAN DIEGO/LAS VEGAS | SAN DIEGO | CXP102051_27_R21F24
CAL00013_2A_1 | 5/22/2018 0:03 | 58.47 | 1.59 | 3846 | CAL00013 | 2200 | 10000 | 490 | 32.7306694 | -117.1596778 | 84.2 | SAN DIEGO/LAS VEGAS | SAN DIEGO | CXP102051_27_R21F24
CAL00013_2A_1 | 5/22/2018 0:04 | 69.89 | 1.83 | 4394 | CAL00013 | 2200 | 10000 | 490 | 32.7306694 | -117.1596778 | 84.2 | SAN DIEGO/LAS VEGAS | SAN DIEGO | CXP102051_27_R21F24
Cell PRB Utilization
(target to be predicted)
Additional cell metrics
Cell information
Snapshot of the training data for cell load prediction
External features:
Active UE count
Cell throughput
Avg UE throughput
1 week ago
1 day ago
(=1 min)
Feature Correlation Matrix
Temporal features:
Instant trend:
Periodic pattern:
Seasonal pattern :
= 1 day, = 1 week
Cell configuration: band, power, bandwidth, …
Day of week, Hour of day

## Slide 9: Cell Load Prediction (2): experiment and evaluation
For longer horizon of 120 mins, DeepAuto showed upto 32% reduction in RMSE compared to naive method, 4% improvement over XGBoost.
  For short horizon of 15 minutes the gains compared to other methods are reduced.
Data Source | t | # instances | RMSE | MAE | MAPE (y>mean) | MAPE (y>mean+std)
PM Counter | 2 hours | ~ 13.2 M | 0.094 | 0.065 | 19.9% | 14.1%
PM Counter | 15 mins | ~ 13.7 M | 0.063 | 0.0425 | 15.30% | 12.50%
CTR/STEM | 1 min | ~ 14.8 M | 0.091 | 0.0604 | 18.47% | 13.73%
Data Source |  | # instances | RMSE | MAE | MAPE (y>mean) | MAPE (y>mean+std)
PM Counter | 2 hours | ~ 13.2 M | 0.094 | 0.065 | 19.9% | 14.1%
PM Counter | 15 mins | ~ 13.7 M | 0.063 | 0.0425 | 15.30% | 12.50%
CTR/STEM | 1 min | ~ 14.8 M | 0.091 | 0.0604 | 18.47% | 13.73%

## Slide 10: RF prediction (1)
The reported RSRQ values are grouped by timestamp (at 5-mins interval) and cell id, and binned into 17 buckets.
Snapshot of the data for prediction
RSRQ PDF :
% of RSRQ measurements in each bin (17 bins in total)
Temporal and external features:
Histogram of RSRQ
Day of week, Hour of day
Minute of day
Instant trend:
Periodic pattern:
Seasonal pattern :
=25, = 1 day, = 0 week
1 day
*note: correlation artifact due to non-continuous data

## Slide 11: RF prediction (2): experiment and evaluation
KL divergence is used as a loss metric for comparing true and predicted distribution.
  where is the number of LTE cells in the testing dataset and is the KL divergence calculated for cell
*Traditional statistical/machine learning methods seem unsuitable for this problem. Thus, baseline performance is not provided for other methods
DeepAuto achieved 75% improvement compared to naive method

## Slide 12: Concluding remarks
Goal
Design scalable
Reusable prediction system
Evaluation
Models show advantage in capturing complex relationships
DeepAuto
A deep learning framework to predict RAN KPI with various time horizons
Accurate forecasting of RAN KPIs represents an essential part LTE/5G RAN automation. We provided an unified, efficient and effective traffic prediction architecture that predicts various RAN KPIs in real time.
We presented the prediction model DeepAuto, hierarchical deep learning framework, that constructively captures spatial, temporal and external factors, as well as network configuration changes in a scalable manner.
Machine learning methods reduce the prediction error by upto 75% compared to the naive method of using recent measurement.

## Slide 14: Results
DeepAuto performs superior compared to other baseline methods in all metrics considered. For 15 min horizon, DeepAuto showed upto 15% improvement in RMSE compared to naive method, 2.5 % improvement compared to random forest and 1.5% improvement compared to XGBoost.
Naive method of using yt􀀀1 as prediction resulted in KL divergence of 0.14 while DeepAuto achieved a KL divergence value of 0.0353 (over 75% improvement compared to naive method).

## Slide 15: Deployment
Build model
eNBs
Data Sources
Batched/
offline data
Batch processing
file based
Kafka API
Model update
Stream processing
Prediction
every 1 min
for all cells
Prediction
Microservice
Apps
Training phase
Prediction phase